## Slide 1: Computer Architecture Experiment
浙江大学计算机学院
2021年9月
Topic 2. Pipelined CPU supporting
exception & interrupt

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of CPU exception & interrupt and its processing procedure.
Master the design methods of pipelined CPU supporting exception & interrupt.
master methods of program verification of Pipelined CPU supporting exception & interrupt.

## Slide 4: Experiment Task
Design of Pipelined CPU supporting exception & interrupt.
  Design datapath
  Design Co-processor & Controller
Verify the Pipelined CPU with program and observe the execution of program

## Slide 5: Pipelined CPU supporting exception & interrupt

## Slide 6: Pipelined CPU supporting exception & interrupt

## Slide 7: Pipelined CPU supporting exception & interrupt

## Slide 8: Pipelined CPU supporting exception & interrupt
Environment Call and Breakpoint
Trap-Return Instructions

## Slide 9: Pipelined CPU supporting exception & interrupt
Machine-mode status register (mstatus) for RV32.
Notes: 非法指令
ECALL
L/S 地址超范围

## Slide 10: Pipelined CPU supporting exception & interrupt
发生异常/中断时，硬件自动经历如下的状态转换：
⚫ 异常指令的PC被保存在mepc中，PC被设置为mtvec。mepc指向导致异常的指令；对于中断，它指向中断处理后应该恢复执行的位置。
⚫ 根据异常来源设置mcause，并将mtval设置为出错的地址或者其它适用于特定异常的信息字。
⚫ 把控制状态寄存器mstatus中的MIE位置零以禁用中断，并把先前的MIE值保留到MPIE中。
⚫ 发生异常之前的权限模式保留在mstatus的MPP域中，再把权限模式更改为M。
Notes: 非法指令
ECALL
L/S 地址超范围

## Slide 11: Pipelined CPU supporting exception & interrupt

## Slide 12: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | 
3 | 00c02283 | C |  | lw x5, 12(x0) | 
4 | 01002303 | 10 |  | lw x6, 16(x0) | 
5 | 01402383 | 14 |  | lw x7, 20(x0) | 
6 | 306850f3 | 18 |  | csrrwi x1, 0x306, 16 | 
7 | 306020f3 | 1C |  | csrr x1, 0x306 | 
8 | 306310f3 | 20 |  | csrrw x1, 0x306, x6 | 
9 | 306020f3 | 24 |  | csrr x1, 0x306 | 
10 | 00000013 | 28 |  | addi x0, x0, 0 | 
11 | 07800093 | 2C |  | addi x1, x0, 120 | 
12 | 30509073 | 30 |  | csrw 0x305, x1 | 
13 | 00000013 | 34 |  | addi x0, x0, 0 | 
14 | 00000073 | 38 |  | ecall | 

## Slide 13: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 00000013 | 3C |  | addi x0, x0, 0 | 
16 | 00000012 | 40 |  | addi x0, x0, 0 | # change to illegal
17 | 00000013 | 44 |  | addi x0, x0, 0 | 
18 | 07f02083 | 48 |  | lw x1, 127(x0) | 
19 | 08002083 | 4C |  | lw x1, 128(x0) | # l access fault
20 | 00000013 | 50 |  | addi x0, x0, 0 | 
21 | 08102023 | 54 |  | sw x1, 128(x0) | # s access fault
22 | 00000013 | 58 |  | addi x0, x0, 0 | 
23 | 00000013 | 5C |  | addi x0, x0, 0 | 
24 | 00000013 | 60 |  | addi x0, x0, 0 | 
25 | 00000013 | 64 |  | addi x0, x0, 0 | 
26 | 00000013 | 68 |  | addi x0, x0, 0 | 
27 | 00000013 | 6C |  | addi x0, x0, 0 | 
28 | 00000013 | 70 |  | addi x0, x0, 0 | 
29 | 00000067 | 74 |  | jr x0 | 

## Slide 14: Instr. Mem.(3)
NO. | Instruction | Addr. | Label | ASM | Comment
30 | 34102cf3 | 78 | trap: | csrr x25, 0x341 | # mepc
31 | 34202df3 | 7C |  | csrr x27, 0x342 | # mcause
32 | 30002e73 | 80 |  | csrr x28, 0x300 | # mstatus
33 | 30402ef3 | 84 |  | csrr x29, 0x304 | # mie
34 | 34402f73 | 88 |  | csrr x30, 0x344 | # mip
35 | 004c8113 | 8C |  | addi x2, x25, 4 | 
36 | 34111073 | 90 |  | csrw 0x341, x2 | 
37 | 30200073 | 94 |  | mret | # 30200073 mret
38 | 00000013 | 98 |  | addi x0, x0, 0 | 
39 | 00000013 | 9C |  | addi x0, x0, 0 | 
40 | 00000013 | A0 |  | addi x0, x0, 0 | 
41 | 00000013 | A4 |  | addi x0, x0, 0 | 

## Slide 15: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 16: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;

## Slide 17: Simulation (1)

## Slide 18: Simulation (2)

## Slide 19: Simulation (3)

## Slide 20: Simulation (4)

## Slide 21: Simulation (5)

## Slide 22: Simulation (6)

## Slide 23: Simulation (7)

## Slide 24: Simulation (8)

## Slide 25: Simulation (9)

## Slide 26: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 27
Thanks!