## Slide 1: Computer Architecture Experiment
浙江大学计算机学院
2021年9月
Topic 2. Pipelined CPU supporting
exception & interrupt

## Slide 2: Outline
Experiment Purpose
Experiment Task
Basic Principle
Operating Procedures
Checkpoints

## Slide 3: Experiment Purpose
Understand the principle of CPU exception & interrupt and its processing procedure.
Master the design methods of pipelined CPU supporting exception & interrupt.
master methods of program verification of Pipelined CPU supporting exception & interrupt.

## Slide 4: Experiment Task
Design of Pipelined CPU supporting exception & interrupt.
  Design datapath
  Design Co-processor & Controller
Verify the Pipelined CPU with program and observe the execution of program

## Slide 5: Revie 4.6 Interruption & Exception
What’s Interruption & Exception ？
Why need interruption & exception？
How to deal with interruption & Exception in RISC V ?
  Transfer control to exception handler & return from exception
  Control status registers
  CSR instructions
  How to write an exception handler ?

## Slide 6: Interruption & Exception
The cause of changing CPU’s work flow :
  Control instructions in program (bne/beq, jal , etc)
  It is foreseeable in programming flow
  Something happen suddenly (Exception and Interruption)
  It is unpredictable
    Call Instructions triggered by hardware
Exception
  Arises within the CPU when execute
  instruction
  e.g., overflow, undefined opcode, syscall, …
Interrupt
  From an external I/O controller
Dealing with them without sacrificing performance is hard

## Slide 7: Why we need interrupt ?
When you double click the mouse ……
When a network package arrives ……
When you want to print a sentence on screen ……
Event external to the running program can interrupt the processor : ex Interruption driven I/O
  polling ----waste a lot of processor time
  Interruption driven I/O
  DMA ---- direct memory access

## Slide 8: Why we need exception ?
Processor can be interrupted by exceptional events that occur while the program is running that are caused by the program itself.
Example:
  Page fault:
    need OS to load the page into the memory from disk, then resume the program
  Memory address fault ( segmentation fault )
  Undefined opcode
    The OS will stop the program and then transfer to other process.

## Slide 9: Handling Exceptions
Save PC of offending (or interrupted) instruction
  In RISC-V: Supervisor Exception Program Counter (SEPC)
Save indication of the problem
  In RISC-V: Supervisor Exception Cause Register (SCAUSE)
  64 bits, but most bits unused
    Exception code field: 2 for undefined opcode, 12 for hardware malfunction, …
Jump to handler
  Assume at 0000 0000 1C09 0000hex
  Entry address in a special register :Suptervisor Trap Vector (STVEC), which can be loaded by OS.

## Slide 10: An Alternate Mechanism
Vectored Interrupts
  Handler address determined by the cause
Exception vector address to be added to a vector table base register:
  Undefined opcode 00 0100 0000two
  Hardware malfunction: 01 1000 0000two
  …: …
Instructions either
  Deal with the interrupt, or
  Jump to real handler

## Slide 11: Handler Actions
Read cause, and transfer to relevant handler
Determine action required
If restartable
  Take corrective action
  use SEPC to return to program (mret)
Otherwise
  Terminate program
  Report error using SEPC, SCAUSE, …
  OS make the choice to transfer to another ready process

## Slide 12: Exceptions in RISC V
  Transfer control to exception handler & return from exception
  Control status registers
  CSR instructions
  How to write an exception handler ?

## Slide 13: Privileged Architecture
Software stack

## Slide 14: Privileged level
Privilege Level in RISC V
  Provide protection between different components of the software stack

## Slide 15: CSR Address Mapping Convention
CSR[11..0] 4096
12 bit encoding space
11: read only
00/01/10: read/write
The lowest privileged level that can access CSR

## Slide 16: 8 important CSR for exception handling
8 CSR :
mtvec ( Machine Trap Vector): jump to this address when exception
mepc (Machine Exception PC): the instruction raise the exception
mcause (Machine exception Cause): which kind of exception(cause)
mie (Machine Interrupt Enable): which exception can be handled or negleted
mip (Machine interrupt pending): pending interruptions (read only register)
mtval (Mahine trap value): error address , illegal instruction, or 0
mscratch ( Machine Scratch):
mstatus ( Machine status) : processor status

## Slide 17: Pipelined CPU supporting exception & interrupt

## Slide 18: mtvec
Store the interruption handler entrance address
The base can be explained according to mode code
  00: PC base
  x1： vector mode， PC  mtval – 1 + 4x ( not required)
base[31..2] mode

## Slide 19: mepc
Save the instruction address when exception raised or interruption happens.
  the PC indicate the instruction that raise the exception
  the instruction need to be executed after back from interruption
    next instruction

## Slide 20: mcause
If mcause[31] == 1 then the trap was caused by an interruption.
Exception code field: a code identifying the last exception.
interruption exception code
31 30 0

## Slide 21: Exception Causes
Address misaligned
Access fault
illegal instruction
Breakpoint
Environment call
Synchronization exception
Asynchronization exception
Software interrupt
Timer interrupt
External interrupt

## Slide 22: Machine Status Register
MIE is an interruption enable (global ) (different from the MIE register )
When an interruption/ exception raised: mstatus[7]  mstatus[3]
When MRET is executed: mstatus[3]  mstatus[7]

## Slide 23: CSR instructions

## Slide 24: CSR instructions
csrrw rd, csr, rs1: tCSRs[csr], CSRs[csr]x[rs1], x[rd]t
csrrs rd, csr, rs1: tCSRs[csr], CSRs[csr] t | x[rs1], x[rd]t
csrrc rd, csr, rs1: tCSRs[csr], CSRs[csr] t & ~x[rs1], x[rd]t
csrrwi rd, csr, zimm[4..0]: x[rd] CSRs[csr], CSRs[csr]zimm
cssrrsi rd,csr,zimm[4..0]: tCSRs[csr], CSRs[csr]t | zimm; x[rd]t
csrrci rd, csr, zimm[4..0]: tCSRs[csr], CSRs[csr]t&~zimm; x[rd]t

## Slide 25: How to Checks for Exceptions(Hardware)
Add test logic
  illegal instruction, load address misaligned, store address misaligned
add control signal
  CauseWrite for mcause
  EPCWrite for mepc
  TVALWrite for mtval
process of control
  mepc  PC( exception) or PC + 4 (interruption)
  mcause  set correspondent bit
  mtval  memory address or illegal instruction
  mstatus.mpie Mstatus.mie; mstatus.mie 0; mstatus.mppmp; mp11
  PC←address of process routine ( mtvec, ex. c0000000 )

## Slide 26: When jump to exception handler ？
Jump to handler
  Assume at 0000 0000 1C09 0000hex
jump when
mstatus.MIE = 1 && mie[i] = 1 && mip [i]= 1

## Slide 27: Ex. Exception handler

## Slide 28: Ex. Exception handler （cont.)

## Slide 29: Pipelined CPU supporting exception & interrupt
Environment Call and Breakpoint
Trap-Return Instructions

## Slide 30: How to back to the exception breakpoint ?
mret
  PC  CSRs[mepc]
  mstatus.MIE mstatus.MPIE
  mp mstatus.MPP

## Slide 31
How to support exception in pipelined CPU ?

## Slide 32: Flow of Instructions During Exception

## Slide 33: Precise Exceptions
If the pipeline can be stopped so that the instructions issued before the faulting instruction complete, then the pipeline is said to implement precise exceptions
  All instructions before the faulting instruction complete
  And instructions following the faulting instruction, including the faulting instruction, do not change the state of the machine.
Under this model, restarting is easy:
  Simply re-execute the original faulting instruction.
  Or, if it is not a resumable instruction, i.e. an integer overflow, start with the next instruction.

## Slide 34: Imprecise Exceptions
Difficult to do when some instructions take multiple cycles to complete
  Some instructions may complete before an exception is detected
  Example
    Multiply r1, r2, r3 ; multiply takes 10 cycles
    Add r10,r11,r12 ; add takes 5 cycles
  Add will complete before multiply is done. If multiply overflows, thenan exception will be raised AFTER the add has updated the value in R10.
  This is an imprecise exception.

## Slide 35: Which stage can exceptions occur in?
Stage Problem exceptions occurring
  IF page fault on instruction fetch;
  misaligned memory access;
  memory protection violation
  ID undefined or illegal opcode
  EX arithmetic exception
  MEM page fault on data fetch;
  misaligned memory access;
  memory-protection violation
  WB none

## Slide 36: Multiple Exceptions in one clock cycle
In Clock Cycle 4, LW can have a data page fault while the ADD has an arithmetic exception
Handled by servicing the page fault and then restarting the LW instruction
The ADD’s arithmetic exception will occur again because the ADD instruction is restarted after the exception is handled

## Slide 37: Multiple Exceptions out-of-order
ADD causes an exception in the instruction fetch stage while LW causes an exception in the memory access stage
If we implement precise exceptions, LW exception must be handled first
This is done by having hardware post exceptions by order of instruction

## Slide 38: Exception ordering
When the instruction is about to exit the pipeline (MEM/WB), any pending exceptions for the instruction are examined.
If an instruction generates multiple exceptions, the exception occurring in the earliest stage takes precedence.
This is done by keeping an exception vector for each instruction:
  If an exception is posted, it is added to the vector and all writes that affect system state are disabled.

## Slide 39: About Exceptions
One of the single messiest parts of designing a modern CPU
  It isn’t pretty, it’s easy to get wrong
  It’s often not too elegant
  It usually takes huge wads of special logic
Further complicated by modern CPU mechanisms
  Deep pipes
  Superscalar --lots of instructions in flight in parallel
  Out-of-order execution
    time order of exceptions  program order of the instructions on which the exceptions happened
  Maintaining illusion of “sequential instruction execution” gets really complicated.

## Slide 40: Implement precise interruption in Pipelined CPU
1、When an exception is raised, there are several instructions flying in the pipeline, how to stop the pipeline at the right place and safely shutdown the pipeline ?
  If an exception is posted, it is added to the vector and all writes that affect system state are disabled
  Record the correspond cause and information ( such as memory address )
2、How to keep the right exception ordering ?
  Trap when there is exception or interruption at the stage of WB

## Slide 41: Pipelined CPU supporting exception & interrupt
发生异常/中断时，硬件自动经历如下的状态转换：
⚫ 异常指令的PC被保存在mepc中，PC被设置为mtvec。mepc指向导致异常的指令；对于中断，它指向中断处理后应该恢复执行的位置。
⚫ 根据异常来源设置mcause，并将mtval设置为出错的地址或者其它适用于特定异常的信息字。
⚫ 把控制状态寄存器mstatus中的MIE位置零以禁用中断，并把先前的MIE值保留到MPIE中。
⚫ 发生异常之前的权限模式保留在mstatus的MPP域中，再把权限模式更改为M。
Notes: 非法指令
ECALL
L/S 地址超范围

## Slide 42: Pipelined CPU supporting exception & interrupt

## Slide 43: Instr. Mem.(1)
NO. | Instruction | Addr. | Label | ASM | Comment
0 | 00000013 | 0 | __start: | addi x0, x0, 0 | 
1 | 00402103 | 4 |  | lw x2, 4(x0) | 
2 | 00802203 | 8 |  | lw x4, 8(x0) | 
3 | 00c02283 | C |  | lw x5, 12(x0) | 
4 | 01002303 | 10 |  | lw x6, 16(x0) | 
5 | 01402383 | 14 |  | lw x7, 20(x0) | 
6 | 306850f3 | 18 |  | csrrwi x1, 0x306, 16 | 
7 | 306020f3 | 1C |  | csrr x1, 0x306 | 
8 | 306310f3 | 20 |  | csrrw x1, 0x306, x6 | 
9 | 306020f3 | 24 |  | csrr x1, 0x306 | 
10 | 00000013 | 28 |  | addi x0, x0, 0 | 
11 | 07800093 | 2C |  | addi x1, x0, 120 | 
12 | 30509073 | 30 |  | csrw 0x305, x1 | 
13 | 00000013 | 34 |  | addi x0, x0, 0 | 
14 | 00000073 | 38 |  | ecall | 

## Slide 44: Instr. Mem.(2)
NO. | Instruction | Addr. | Label | ASM | Comment
15 | 00000013 | 3C |  | addi x0, x0, 0 | 
16 | 00000012 | 40 |  | addi x0, x0, 0 | # change to illegal
17 | 00000013 | 44 |  | addi x0, x0, 0 | 
18 | 07f02083 | 48 |  | lw x1, 127(x0) | 
19 | 08002083 | 4C |  | lw x1, 128(x0) | # l access fault
20 | 00000013 | 50 |  | addi x0, x0, 0 | 
21 | 08102023 | 54 |  | sw x1, 128(x0) | # s access fault
22 | 00000013 | 58 |  | addi x0, x0, 0 | 
23 | 00000013 | 5C |  | addi x0, x0, 0 | 
24 | 00000013 | 60 |  | addi x0, x0, 0 | 
25 | 00000013 | 64 |  | addi x0, x0, 0 | 
26 | 00000013 | 68 |  | addi x0, x0, 0 | 
27 | 00000013 | 6C |  | addi x0, x0, 0 | 
28 | 00000013 | 70 |  | addi x0, x0, 0 | 
29 | 00000067 | 74 |  | jr x0 | 

## Slide 45: Instr. Mem.(3)
NO. | Instruction | Addr. | Label | ASM | Comment
30 | 34102cf3 | 78 | trap: | csrr x25, 0x341 | # mepc
31 | 34202df3 | 7C |  | csrr x27, 0x342 | # mcause
32 | 30002e73 | 80 |  | csrr x28, 0x300 | # mstatus
33 | 30402ef3 | 84 |  | csrr x29, 0x304 | # mie
34 | 34402f73 | 88 |  | csrr x30, 0x344 | # mip
35 | 004c8113 | 8C |  | addi x2, x25, 4 | 
36 | 34111073 | 90 |  | csrw 0x341, x2 | 
37 | 30200073 | 94 |  | mret | # 30200073 mret
38 | 00000013 | 98 |  | addi x0, x0, 0 | 
39 | 00000013 | 9C |  | addi x0, x0, 0 | 
40 | 00000013 | A0 |  | addi x0, x0, 0 | 
41 | 00000013 | A4 |  | addi x0, x0, 0 | 

## Slide 46: Data Mem.
NO. | Data | Addr. | Comment
0 | 000080BF | 0 | 
1 | 00000008 | 4 | 
2 | 00000010 | 8 | 
3 | 00000014 | C | 
4 | FFFF0000 | 10 | 
5 | 0FFF0000 | 14 | 
6 | FF000F0F | 18 | 
7 | F0F0F0F0 | 1C | 
8 | 00000000 | 20 | 
9 | 00000000 | 24 | 
10 | 00000000 | 28 | 
11 | 00000000 | 2C | 
12 | 00000000 | 30 | 
13 | 00000000 | 34 | 
14 | 00000000 | 38 | 
15 | 00000000 | 3C | 
NO. | Instruction | Addr. | Comment
16 | 00000000 | 40 | 
17 | 00000000 | 44 | 
18 | 00000000 | 48 | 
19 | 00000000 | 4C | 
20 | A3000000 | 50 | 
21 | 27000000 | 54 | 
22 | 79000000 | 58 | 
23 | 15100000 | 5C | 
24 | 00000000 | 60 | 
25 | 00000000 | 64 | 
26 | 00000000 | 68 | 
27 | 00000000 | 6C | 
28 | 00000000 | 70 | 
29 | 00000000 | 74 | 
30 | 00000000 | 78 | 
31 | 00000000 | 7C | 

## Slide 47: Test Bench
RV32core core(
.debug_en(1'b0),
.debug_step(1'b0),
.debug_addr(7'b0),
.debug_data(),
.clk(clk),
.rst(rst),
.interrupter(1'b0)
);
initial begin
clk = 0;
rst = 1;
#2 rst = 0;
end
always #1 clk = ~clk;

## Slide 48: Simulation (1)

## Slide 49: Simulation (2)

## Slide 50: Simulation (3)

## Slide 51: Simulation (4)

## Slide 52: Simulation (5)

## Slide 53: Simulation (6)

## Slide 54: Simulation (7)

## Slide 55: Simulation (8)

## Slide 56: Simulation (9)

## Slide 57: Checkpoints
CP 1:
  Waveform Simulation of the Pipelined CPU with the verification program
CP 2:
  FPGA Implementation of the Pipelined CPU with the verification program

## Slide 58
Thanks!