## Slide 1: Computer Architecture ----A Quantitative Approach
陈文智
浙江大学计算机学院
chenwz@zju.edu.cn

## Slide 3: Multithreaded Software
Process
  Each process has its unique address space
  Can consist of several threads
Thread – each thread has its unique execution context:
  Its own PC + registers + stack
  All threads within a process share same address space
  Private heap is optional
Multithreaded app’s: process broken into threads
  Increase concurrency
  Partial blocking
  Centralized (smarter) resource management (by process)

## Slide 5: Multithreaded Architecture
Processor capable of executing multiple software threads
  Can execute “simultaneously”
    Thread can be HW switched without OS control
  Shared resource
    Sharing -> better resource utilization -> better throughput
  Can belong to the same process – but not have to !

## Slide 8: Thread scheduling policies

## Slide 9: Denelcor HEP
The Denelcor HEP was a uniform shared memory multiprocessor that used fine-grain multithreading to tolerate memory latency, synchronization latency, and even functional unit latency.

## Slide 10: Tera MTA

## Slide 11: MTA Architecture

## Slide 12: Coarse-Grain Multithreading

## Slide 13: IBM Power RS64-IV (2000)

## Slide 14: Multithreading design choices

## Slide 15: Super scalar Machine Efficiency
Cache misses

## Slide 16: Vertical Multithreading

## Slide 17: Chip Multiprocessing

## Slide 18: Ideal Superscalar Multithreading

## Slide 19: O-o-O Simultaneous Multithreading

## Slide 20: Basic Out-of-order Pipeline

## Slide 21: SMT Pipeline

## Slide 22: Design Challenges in SMT
Trade-off between fine-grained implementation performance and single-thread performance.
  preferred thread : might sacrifices throughput
  Less likely to have a mix of instructions from several threads.
  Maximize single-thread performance, should fetch as far ahead as possible, and have the fetch unit free when a branch is mispredicted or miss occur in prefetch buffer.

## Slide 23: Design Challenges in SMT
A larger register file to hold multiple context
Not affecting the clock cycle, such as in instruction issue, in instruction completion.
Ensuring that Cache and TLB conflicts do not cause performance degradation.

## Slide 24: Power 5 with SMT support vs Power 4
Increasing the associativity of L1 I-cache and ITLB
Adding per-thread load and store queues
Increasing the size of L2 and L3
Adding separate instruction prefetch and buffering
Increasing virtual registers from 152 to 240
Increasing size of several issue queues

## Slide 25: Pentium-4 Hyperthreading

## Slide 26: HT Technology Architecture
Front End
  Execution trace cache
  Microcode store ROM (MSROM)
  Instruction translation look-aside buffer (ITLB) and branch prediction
  IA-32 instruction decode
  Micro-op queue
Bus unit
3rd level cache
Optional server product
2nd level cache
1st level cache
4 way
Fetch/
Decode
Trace Cache
MS ROM
OOO
Execution
Retirement
BTBs/
Branch Prediction
System Bus

## Slide 27: Front End
Responsible for delivering instruction to the later pipe stages
Trace cache hit
  When the requested instruction trace is present in trace cache
Trace cache miss
  Requested instruction is brought in the trace cache from L2 cache

## Slide 28: Trace Cache (TC) Hit - Front End
Two sets of instruction pointers
Two logical processors arbitrates access to TC every clock cycle
If one logical processor stalled, then other logical processor can use the full bandwidth of TC
IP
IP
Trace Cache
Micro-Op Queue

## Slide 29: Trace Cache Miss - Front End
Queue
Micro-op Queue
ITLB
L2 Access
Decode
L2 Access
Buffer
Decode
Trace Cache Fill
(ping-pong)
(ping-pong)
(ping-pong)

## Slide 30: HT Technology Architecture
  Back End
  Allocator
  Register rename
  Instruction scheduling
  Execution units
  Retirement
Bus unit
3rd level cache
Optional server product
2nd level cache
1st level cache
4 way
Fetch/
Decode
Trace Cache
MS ROM
OOO
Execution
Retirement
BTBs/
Branch Prediction
System Bus

## Slide 31: Detailed Pipeline
L1 D Cache
Sched.
Register
Rename
Allocate
Micro-op Queue
Queue
Register Read
Execute
Register Write
Retire

## Slide 32: Allocator - Back End
Allocates many of the key machine buffers including
126 re-order buffer entries
128 integer and floating point physical registers
48 load 24 store buffers
When HT Technology is enabled, each logical processor can use maximum of 63 re-order buffer entries, 24 load buffers and 12 store buffers

## Slide 33: Register Rename - Back End
There are two Register Alias Tables (RAT) for each processor
Rename done in parallel with allocator logic
Once done, micro-ops are placed into two sets of queues: MIAQ (memory instruction address queue) and GIAQ (general instruction address queue)
Queues are partitioned such that micro-ops from each logical processor can use at most half the entries

## Slide 34: Instruction Scheduling - Back End
Five schedulers are used to schedule different types of micro-ops
Both MIAQ and GIAQ send micro-op to five schedulers as fast as they can
Each scheduler has its own scheduler queue
Micro-ops are simply evaluated based on dependent inputs and availability of execution resources
To avoid deadlock, there is a limit on number of active entries that a logical processor can have in scheduler’s queue

## Slide 35: Execution units - Back End
After execution, micro-ops are placed in re-order buffer. It decouples execution stage from retirement stage
Re-order buffer (ROB) is partitioned such that each logical processor can use half entries

## Slide 36: Retirement - Back End
Tracks when micro-ops from two logical processors are ready to be retired, then retires the micro-ops by alternating between two logical processors

## Slide 37: HT Technology Architecture
  Memory Subsystem
  DTLB
  L1 data cache
  L2 unified cache
  L3 unified cache
Bus unit
3rd level cache
Optional server product
2nd level cache
1st level cache
4 way
Fetch/
Decode
Trace Cache
MS ROM
OOO
Execution
Retirement
BTBs/
Branch Prediction
System Bus

## Slide 38: DTLB - Memory Subsystem
Tagged resource
Each entry in dual translation lookaside buffer (DTLB) includes a logical processor ID tag
Each processor has reservation register to ensure fairness and forward progress in processing DTLB misses

## Slide 39: Memory Subsystem L1/2/3 Cache
Both logical processors can share all entries in all three levels of cache

## Slide 40: Bus
Logical processors are treated on first-come first-serve basis. Priority is not given to any logical processor
Distinction between requests from two logical processors are maintained
Requests to APIC and interrupt delivery resources are unique and separate per logical processor

## Slide 41: Speculative, Out-of-Order Superscalar Processor

## Slide 42: Granularity of Multithreading

## Slide 43: Sun T1 Multiprocessor
Focus on Thread Level Parallelism
Commercial application oriented
Small single-issue core employ multithreading
Multi core on chip

## Slide 44: Single Thread Design
L2 cache is getting larger with less performance contribution
Power efficiency decrease
Hot-spot
Lower processor utilization

## Slide 45: Single Thread design multiple issue

## Slide 46: Hardware Multi Threading

## Slide 47: Chip Multithreading

## Slide 48: Why CMT works ?

## Slide 49: T1 Architecture
8 core/chip
4 Treads/core
1 FPU shared for 8 cores
Core connected via crossbar switch(134.4GB/s)
High-bandwidth, 12-way associative 3MB L2 cache
4 DDR2 channels (23GB/s)
Power < 80W
`300M transistors
378 mm2 die
1 core

## Slide 50
L1 cache: 16KB Icache, 32B line; Dcache, 8KB, 16B line; 4-way set associative, 64B block, L1 miss penalty=23 cycles,
L2 cache: 4 banks, each 750KB, 64B block, L2 miss penalty = 110 cycles
L1 cache coherence is enforced by directory associate with each L2 cache block
Memory controller on chip to decrease miss penalty

## Slide 51: Compare with SMP
BTU: british theraml Unit

## Slide 52: Core structure
4 threads /core
Single issue
6 stage pipeline
Unique resources/thread
  Registers
  Portions of I-fetch datapath
  Store and Miss buffers
Resource shared by 4 threads
  Caches, TLBs, Exe Units
  Pipeline registers and Data path
Core area = 11mm2 in 90nm
MT adds ~20% area to core

## Slide 53: T1 processor core pipeline

## Slide 54: Thread Selection Policy
Switch among available ( ready to run) threads every cycle
  Priority given to least-recently-executed thread
Thread becomes not-ready-to-run due to:
  Long latency operations like load, branch, mul, or div ( load, branch incur 1 3-cycle delay )
  Pipeline stall when cache miss, trap, or structure hazard

## Slide 55: Instruction Fetch/Switch/Decode Unit (IFU)
I-cache
  16KB data, 4ways, 32B line
  Single-ported Instruction Tag
  Dual-ported(1R/1W) Valid-bit array
  Invalidate operations access Valid-bit array, not instruction Tags
  Pseudo-random replacement
Fully associative Instruction TLB
  64 entries, Page sizes: 8K, 64K, 4M, 256M
  Multiple hits in TLB prevented by doing auto-demap on fill
2 instructions fetched each cycle

## Slide 56: Windowed Int Register file
5KB 3R/2W/1T structure
  >640 64b regs
Only the 32 registers from current window is visible to thread
8 global + 24 window register
Window changing in background under thread switch
Single cycle R/W accwss

## Slide 57: Execution Units
Single ALU and shifter. ALU reused for branch address and virtual address calculation.
Integer Multiplier
  5 clock latency, throughput of ½ per cycle
  Constrains accumulate function for Mod Arithmetic
  1 integer mul allowed outstanding per core
  Multiplier shared between Core Pipe and Modular Arithmetic unit on a round robin basis
Simple divider, with one divide outstanding per core
Thread issuing a MUL/DIV will rollback and switch out if mul/div units is occupied.

## Slide 58: Load Store Unit (LSU)
D-Cache complex
  8KB data, 4 ways, 16B line
  Single ported Data Tag
  Dual ported(1R/1W) Valid bit array
  Pseudo-random replacement
  Load are allocating, stores are non allocating
8 entry store buffer per thread, unified into single 32 entry array, with RAW bypassing

## Slide 59: LSU (continued)
Crossbar interface
  LSU priorities requests to the crossbar for FPops, streaming ops, I and D misses, stores and interrupts.
Request priority
  Imiss > ldmiss > stores, {fpu, strm, interrupt}
  Packed assembly for pcx.
Handles return from crossbar and maintains order for cache updates and invalidates.

## Slide 60: Other Functions
Support for up to 64 pending interrupts per thread
Support for 6 trap levels. Traps cause pipeline flush.
Floating Point
  The thread switch out when detecting ans FPop
  FPop is further decoded and FRF is read
  FPop with operands are packetized and shipped over the crossbar to the FPU
  FPU returned the result via crossbar
  Write back to FRF and thread restart

## Slide 61: Cross Bar
Each requestor queues up to 2 packets per destination
3 stage pipeline: request, arbitrate and transmit
Oldest requestor first
Core to cache bus;
  Address+double word store
Cache to core bus
  16B line 32B Icache line fill delivered in 2 back to back clock cycles

## Slide 62: L2 Cache
3MB, 4-way banked, 12-way associative, writeback
64B line size, 64B interleaved between banks
Latency: 8 clocks for load, 9 clocks for I-miss, critical chunk first
16 outstanding misses per bank  64 total
Coherence maintained by shadowing L1 tags in an L2 directory structure
L2 is global visibility. DMA from IO is serialized write traffic from cores in L2
L2 has a 8-stage pipeline ( C1-C8)

## Slide 63: L2 Cache - Directory
Directory shadows L1 tags
  2048 entries, half-half for Icache and Dcache
  L1 set index and L2 bank interleaving is such that ¼ of L1 entries come from each L2 bank
  On and L1 miss, the L1 replacement way and set index identify the physical location of tag
  On a store, write invalidate will be done
    Invalidate operation are pointer to the physical location of L1. ( no tag lookup in L1)
    An acknowledgement packet is sent to the request CPU, an invalidation packet sent to all other core

## Slide 64: L2 Cache Single Bank
Arbiter ( instruction from CCX, DMA instruction, stall signals from pipeline, instruction from FB and MB )
L2 tag
L2 VUAD array –Valid, Used, Allocated( set when a line is picked for replacement) Dirty
L2 data
Input Queue ( 16 entry FIFO ) – packets arriving on the PCX
Output Queue ( 16 entry FIFO ) – operations waiting for access to CPX(cache-to-processor interface)
Snoop input Queue ( 2-entry FIFO )
Miss buffer (MB) (L2 misses, same line address with previous miss or write-back buffer, atomics and partial stores etc.)
Fill buffer ( temp store data from DRAM )
Write-back buffer
Remote DMA write buffer ( 4 entry ) for DMA write
L2 cache directory –coherency management and maintain inclusive property

## Slide 65: Coherence/consistency
Load update directory & fill the L1 on return
Stores are non-allocating in L1
  TSO, PSO, RMO ( one TSO store outstanding to L2 per thread)
  Check directory and determine L1 hit
  Directory send store ack/inv to core
  Store update happens to Dcache on store ack
Crossbar orders responses across cache banks
3 atomic instructions are processed by L2 cache
  LDSTUB, SWAP, Compare and swap(CAS)
  Two passes down to cache pipeline

## Slide 66: On chip Mem controller
4 independent DDRII DRAM channels
Up to 128GB memory size
25GB/s peak bandwidth
Schedules across 8 rds + 8 writes
128+16b interface, chipkill support, correction, byte error detection
Designed to work from 125-200Mhz

## Slide 67: T1 Performance

## Slide 68: Conclusion
Sun T1 provides much better performance in terms of performance/watt, especially for TPC-C-like and SPECJBB05 benchmark.
TLP approach is much more power efficient than an ILP-intensive approach for multithreaded applications.
CMT may provide a way to increase performance in a power efficient fashion.

## Slide 69
THANK YOU
THANK YOU